## Slide 1
Microcentrifuge tube
Vortex mixer
Centrifuge
Rotor
Pipette
Tip
Equipment
Tubes
Pipette Settings
0
4
5.5
45.5 µL
P200
0
2
0
2 µL
P20
0
1
4
14 µL
P200
0
8
7.5
87.5 µL
P200
0
2
3
23 µL
P200
PCR tubes
Thermal cycler
2
0
0
2 µL
P2
Illustrations created with BioRender.com

## Slide 2
PCR: Materials Needed
EQUIPMENT
Thermal cycler
Vortex mixer
Centrifuge
Mobile device
REAGENTS
(2) DNA from arthropods (Lab 2)
(2) DNA from control arthropods (Lab 2)
(+) DNA Control
Sterile, nuclease-free water
Taq Master Mix
CO1F (Arthropod forward) primer
CO1R (Arthropod reverse) primer
WSpecF (Wolbachia forward) primer
WSpecR (Wolbachia reverse) primer
MATERIALS
Nitrile gloves
Squirt bottle with 70% ethanol
(12) 0.2 ml PCR tubes
Rack for PCR tubes
(2) 1.5 ml tubes
Rack for 1.5 ml tubes
Waste cup for tips
20 μl pipette & tips
200 μl pipette & tips
Sharpie, fine-tipped
Storage box for PCR tubes
Colored lab tape
Optional: Lab tray
PCR PROGRAMS
1 cycle
2 min @ 94 C
30 Cycles
30 sec @ 94 C
45 sec @ 49 C
60 sec @72 C
1 cycle
10 min @ 72 C
Hold @ 4 C
Initial Denaturation
Denaturation
Annealing
Elongation
Final Extension
1 cycle
2 min @ 94 C
30 Cycles
30 sec @ 94 C
45 sec @ 55 C
60 sec @72 C
1 cycle
10 min @ 72 C
Hold @ 4 C
Arthropod
Wolbachia